## Slide 1: NETAPI: User Space API for networking Release 1.0
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Update Design: 2/1/12
Notes: <number>

## Slide 2
07/29/26
<number>
Transport: Fast Path Stacks – General & Enhanced (one or more ARM cores)
07/29/26
<number>
NETAPI
GLUE Layer
General FAST PATH on ARM core(s)
E.G. 6WIND
PKTLIB
PA LLD
SA LLD
QM LLD
SMP KERNEL
NETCP | Switch | QM | CPPI DMA
TIMER
PKT IO
Config
Scheduler
UIO | Timer | CacheManagement |
CPPI DMA
Utilities
General
Fast Path
Configuration
(shared mem)
RX
P
K
T
s
I
P
C
T
I
M
E
R
s
Side
Band
ACC
Callbacks
TX
Pkt
IPC
NETCP
Config
Security
NWAL

## Slide 3
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
NETCP API
Ingress Network Packets from PA
Accelerator Completion from SA
IPC:
  Packets from Slow Path (SP)
Configuration commands from SP
App data for egress
Misc ipc, core2core
Figure 2: NETCP API Context on ARM cores
Timer
PKT
RX
CB
ACC
CB
IPC
RX Call back
Timers
N
et
Pkts
IPC
ACC
Calls

## Slide 4: NETAPI (User space networking API): Functional Areas
General Configuration, Startup, shutdown
Scheduling
  Main entry point. ( more of a sample )
Timers
  Set/cancel timers
Pkt buffer library
  Alloc/free
Pkt I/O
  Put pkts, get pkts
  For network,
  Inter Processor Communication (IPC)
NETCP Security
  Setup SAs, RX policies, sideband crypto
Other NETCP Configuration and Control
  Add mac interface
  Add IP
  General Classifier
  Statistics
Utilities
  Cache management
  Synchronization primitives
  Physical memory/peripheral region mapping
Utility Kernel Module
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: <number>

## Slide 5: General Configuration and Startup
Does global (SOC level), core level and thread level initialization
Need to call for each thread
  One thread per core is targeted use case
  Threads have to be in same process (for Release 1 (Appleton) )
    Goal to allow multiple processes in future using Linux shared memory for globals. (target is wp3/ Kepler2)
  Multiple threads in one CPU supported with compile time option to yield CPU when polling -> MARCH RELEASE
Returns handle to be used in other NETAPI calls..
Main Functions:
  NETAPI_T handle= netapi_init( SOC_MASTER | CPU_MASTER ) :: setup instance
  netapi_shutdown( NETAPI_T ) :: shutdown instance
  void netapi_netcpPoll ( NETAPI_T ) :: poll the netcp configuration responses
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 6: General Configuration and Startup (continued)
Pktlib_HeapIfTable * netapi_getPktlibIfTable (void)
int netapi_getBufMemRemainder (void)
int netapi_getDescRemainder (void) static
NETCP_CFG_FLOW_HANDLE_T netapi_getDefaultFlow (NETAPI_T p) static
NETCP_CFG_ROUTE_HANDLE_T netapi_getDefaultRoute (NETAPI_T p)
static void * netapi_getCookie (NETAPI_T p)
static void netapi_setCookie (NETAPI_T p, void *cookie)
void netapi_netcpPoll (NETAPI_T p)
int netapi_registerHeap (NETAPI_T p, Pktlib_HeapHandle h)
int netapi_unregisterHeap (NETAPI_T p, Pktlib_HeapHandle h)
void netapi_poll_heapGarbage (NETAPI_T p)
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 7: Scheduling
Optional: app can run with its own scheduler, using lower level routines (xxx_poll to check for events).
  TUNE_NETAPI_INCLUDE_SCHEDULER to include scheduler in library
If it is going to be used, need to have a scheduler instance for each thread (ideally one thread per core but should work with multiple threads per core w/ compile time option)..
Functions:
  Startup and configuration of a scheduler instance. Returns instance handle
    NETAPI_SCHED_HANDLE_T * netapi_schedOpen (NETAPI_T n, NETAPI_SCHED_CONFIG_T *p_config, int *p_err)
  Update configuration of a running scheduler (not implemented)
    int netapi_schedControl (NETAPI_SCHED_HANDLE_T *s, NETAPI_SCHED_CONFIG_T *p_config, int *p_err)
  Main entry point – runs until completion configuration defined in schedOpen is met or schedShutdown() is called. This implements the event poll loop. Calls registered callbacks when events arrive.
    int netapi_schedWaitForEvents (NETAPI_SCHED_HANDLE_T *s, int *p_err)
  Shutdown the scheduler:
    int netapi_schedShutdown (NETAPI_SCHED_HANDLE_T *s, NETAPI_SCHED_SHUTDOWN_T *p_close, int *p_err)
  Uitlity to return netapi instance handle associated with this scheduler instance
    static NETAPI_T netapi_schedGetNetapiHandle (NETAPI_SCHED_HANDLE_T *s)
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: <number>

## Slide 8: Scheduling example:
//*** STARTUP CODE ***
//general configuration
nh= netapi_init( MASTER)
..
// configure other API subsystems
Xx_open(); xx_configure()
..
//scheduler
sh= neatpi_schedOpen(nh, ..)
//!! give up control to NETCP_API here!!
netapi_schedWaitForEvents(sh); //does not return until netapi_schedShutdown() is called or configured duration is reached
.//. Shut down code here
Xx_close( )
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
//*** Callback for some event***
… do event processing ..
If (we want to shutdown)
  netapi_schedShutdown_close(sh )
return ; //back to scheduler loop

## Slide 9: Scheduling (application controlled)
Scheduling module is optional. If not used, application will control main loop (per thread/core):
Application loop will need to call individual library poll routines:
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
//poll all pktio channels we have open in RX mode
pktio_pollAll( .., &err);
//poll pktlib garbage collections for registered heaps..
netapi_pollHeapGarbage( .. &err);
//timers (local and global)
netapi_TimerGroupPollAll( );
//poll NETCP/PA control channels
netapi_netcpPoll((NETAPI_T) s->back);

## Slide 10: Scheduling house keeping callback
Scheduler can be configured to callback to housekeeping function periodically (based on number of poll cycles).
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 11: Timers & Timestamps
64 bit time stamp available
  static unsigned long long netapi_getTimestamp (void)
  Runs at CPU clk/6 [ ticks per second available from: netapi_getTicksPerSec() ]
Timers organized in groups with same characteristics:
  Local/global
  Expected to fire versus expected to be cancelled
  Scheduling resolution ( expressed in timestamps)
  Same callback function (required if we are to deliver a block of fired timers to app)
  Same tolerance window
Timer Group APIs:
  Creates a timer group [only one timer group can be created in Release 1]
    NETAPI_TIMER_GROUP_HANDLE_T netapi_TimerGroupCreate (NETAPI_T netHandle, char *name, NETAPI_TIMER_CB_T cb, int local, int exp2cancel, int timerTicksPerGroupTick, int timerTolerence, int maxTimers, int *pErr)
  Starts a timer in the group
    NETAPI_TIMER_T netapi_TimerGroupStartTimer (NETAPI_TIMER_GROUP_HANDLE_T th, void *cookie, uint64_t offs2fire, int *pErr)
  Cancels a timer in the group
    void netapi_TimerGroupCancel (NETAPI_TIMER_GROUP_HANDLE_T th, NETAPI_TIMER_T timerId, int *pErr)
  (Not yet implemented)
    NETAPI_TIMER_GROUP_HANDLE_T netapi_TimerGroupOpen (NETAPI_T netHandle, char *name, NETAPI_TIMER_CB_T cb, int *pErr)
    void netapi_TimerGroupClose (NETAPI_TIMER_GROUP_HANDLE_T th, int *pErr)
    void netapi_TimerGroupDelete (NETAPI_TIMER_GROUP_HANDLE_T th, int *pErr)
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: <number>

## Slide 12: More on timers
Poll the timers registered to the NETAPI instance
  int netapi_TimerGroupPollAll (NETAPI_T nh, NETAPI_TIMER_FILTER_T f, int maxTimers)
Fired timer access:
  Callback function registered at timer create/open
    typedef void(*) NETAPI_TIMER_CB_T(NETAPI_TIMER_GROUP_HANDLE_T th,int n_fired,NETAPI_TIMER_LIST_T fired_list,uint64_t currentTime)
  Will return a list of timers that have fired
  Use iterators to access list of fired timers:
    void* netapi_TimerGetCookie ( NETAPI_TIMER_T timer ) //returns user data associated with timer
    NETAPI_TIMER_T netapi_TimerGetFirst ( NETAPI_TIMER_LIST_T list )
    NETAPI_TIMER_T netapi_TimerGetNext ( NETAPI_TIMER_LIST_T list, NETAPI_TIMER_T prev )
Release 1 Limitations:
  Only one timer group supported
  Tolerance parameter not used
  Can’t delete/close timer group
  Cancelled timers garbage collected later .. (expect2fire implied)
07/29/26. n. n
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 13: Timer Lib Examples
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
//create a timer group
ourTimerBlock = netapi_TimerGroupCreate(
netapi_handle,
"our1sttimer",
our_timer_cb, //callback
0, //1 if timers local to thread
0, //1 if expect to cancel
netapi_getTicksPerSec()/1000, /* 1 msc resolution for these timers */
netapi_getTicksPerSec()/5000, /* would like .5 msc tolerence */
10, //small # of timers to test garbage collection
&err);
if (err) {printf("timergroupcreate failed %d\n",err); exit(1);}
//start a timer
t1 = netapi_TimerGroupStartTimer(
ourTimerBlock,
(void *) 1, //cookie (application defined)
100LL, //timer group ticks
&err);
//cancel a timer
netapi_TimerGroupCancel(th,t1,&err);
//process fired timers (this callback is registered in TimerGroupCreate()
void our_timer_cb( NETAPI_TIMER_GROUP_HANDLE_T th,
int n_fired, NETAPI_TIMER_LIST_T fired_list, uint64_t currentTime)
{
int i;
NETAPI_TIMER_T tx;
int cookie;
tx = netapi_TimerGetFirst(fired_list);
for(i=0;i<n_fired;i++) {
cookie = (int) netapi_TimerGetCookie(tx);
tx = netapi_TimerGetNext(fire_list, tx);
} …
}

## Slide 14: Packet Buffer Library
Struct TI_PKT // a TI packet buffer.
Extern void * netapi_segment_allocate(size. flags)
Extern void netapi_segment_free(ptr)
extern int32_t Pktlib_sharedHeapInit (netcp_api_handle void);
extern Pktlib_HeapHandle Pktlib_createHeap (netcp_api_handle, const char* heapName,
Qmss_MemRegion memRegion,
uint8_t sharedHeap,
uint32_t dataBufferSize,
uint32_t numPkts,
uint32_t numZeroBufferPkts,
Pktlib_HeapIfTable* heapInterfaceTable);
extern Ti_Pkt* Pktlib_allocPacket(Pktlib_HeapHandle heapHandle, uint32_t size);
extern void Pktlib_freePacket(Ti_Pkt* pPkt);
extern Ti_Pkt* Pktlib_packetMerge(Ti_Pkt* pPkt1, Ti_Pkt* pPkt2, Ti_Pkt* pLastPkt);
extern int32_t Pktlib_clonePacket(Ti_Pkt* ptrPktOrig, Ti_Pkt* ptrClonePacket);
extern int32_t Pktlib_splitPacket(Ti_Pkt* pOrgPkt, Ti_Pkt* pNewPkt,
uint32_t splitPacketSize,
Ti_Pkt** pPkt1,
Ti_Pkt** pPkt2);
extern Pktlib_HeapHandle Pktlib_findHeapByName (netcp_api_handle const char* heapName);
extern void Pktlib_getHeapStats(Pktlib_HeapHandle heapHandle, uint32_t* numFreeDataPackets,
uint32_t* numZeroBufferPackets,uint32_t* numPacketsinGarbage);
extern void Pktlib_garbageCollection(Pktlib_HeapHandle heapHandle);
+ inline functions/macros to get at packet buffer fields. Etc.
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: <number>

## Slide 15: Pktlib continued
What is a TI_PKT?
  Descriptor plus optional linked packet buffer(s)
  Wraps our packet-aware DMA descriptor structure
  descriptors are pushed/popped to/from hardware queues
  Descriptors and buffers can be in different memory regions
What is a heap?:
  Blocks of memory carved up into packet buffers [of fixed size] and descriptors
    ID of descriptor area passed in at create time: Must use NETAPI_GLOBAL_REGION
    Pointer to malloc/free functions for buffers is passed in at create time. Must use interface table provided by NETAPI
  Create function builds two types of TI_PKTS: those without buffers and those with buffers (that are malloc’d from provided routine).
  A free (HW) queue #1 for TI_PKTS with packet buffers.
    Free TI_PKTS with packet buffers are placed on this queue
    Pointer to this free queue is in descriptor so that h/w (NETCP) knows how to free.
  A free (HW) queue #2 for TI_PKTS without packet buffers
    Free TI_PKTS without packet buffers are placed on this queue
  A (HW) garbage queue -> this is used to hold clones freed by hw
  Garbage collection routine needs to be called periodically to get clones back onto free queue #1,2.
  NETCP knows how to free TI_PKTS by placing on correct free queue.
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 16: Pktlib continued..
Clone is supported, uses garbage collection to recover cloned pieces from hardware
  clone of clone is supported, etc
  this can be used to implement a “hw don’t free” option
Split/merge function can be used to insert headers.
  No concept of moving internal pointer to data to skip over headers.
Netapi_init() will call the pktlib init functions.
Netapi_init will create some heaps at init time with well known names for application to use.
  pktlib_findHeapByName(“netapi”)
Application may want to create other heaps for IPC, etc .
  Note: release 1 scheduler does not poll garbage queue for application created heaps.
TI_PKT: wrapper for our descriptor format; will give macros, utilities to get at length, buffer (s), etc.
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: <number>

## Slide 17: PKTLIB example
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
/* create netapi */
netapi_handle = netapi_init(NETAPI_SYS_MASTER);
/* open the main heap */
OurHeap = Pktlib_findHeapByName("netapi");
if (!OurHeap) {printf("findheapbyname fail\n"); exit(1);}
//allocate packet
Ti_Pkt * b=Pktlib_allocPacket(OurHeap,PKT_LEN);
..
//extract buffer associated with packet
Pktlib_getDataBuffer(b,(uint8_t**)&buffer,&len);
/* set the pkt length */
Pktlib_setPacketLen(tip, len);..
/* free a packet*/
Pktlib_freePacket(tip);

## Slide 18: Packet I/O Library
PKTIO Channel (hw queue).
  One way connection, either rx or tx ( could support rx and tx in some cases ).
  Used for:
    Tx pkts to NETCP
    rx pkts from NETCP (minimum one but possibly multiple rx queues)
    Pkts from slow path (one or more queues)
    Ipc messages from SP
    Ipc messages to other cores (if needed)
    [internally for accelerator callbacks]
    Data segments from application layers for egress.
// Create a PKTIO Channel
  PKTIO_HANDLE_T * pktio_create (NETAPI_T netapi_handle, char *name, PKTIO_CB cb, PKTIO_CFG_T *p_cfg, int *err)
//Open a PKTIO Channel (that has already been created)
  PKTIO_HANDLE_T * pktio_open (NETAPI_T netapi_handle, char *name, PKTIO_CB cb, PKTIO_CFG_T *p_cfg, int *err)
NOT PRESENT IN RELEASE 1.
  void pktio_control (PKTIO_HANDLE_T *channel, PKTIO_CB cb, PKTIO_CFG_T *p_cfg, PKTIO_CONTROL_T *p_control, int *err)
  void pktio_close (PKTIO_HANDLE_T *channel, int *err)
  void pktio_delete (PKTIO_HANDLE_T *channel, int *err)
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: <number>

## Slide 19: Packet I/O Library (continued)
Channel Configuration:
  typedef struct PKTIO_CFG_Tag {
    #define PKTIO_R 0x1
    #define PKTIO_W 0x2
    #define PKTIO_RW (PKTIO_R | PKTIO_W)
    int flags1;
    #define PKTIO_LOCAL 0x2
    #define PKTIO_GLOBAL 0x1
    #define PKTIO_PKT 0x4 //define this if this q is for NETCP RX
    int flags2;
    //for create
    #define PKTIO_Q_ANY -1
    int qnum;
    //for poll
    int max_n;
  }PKTIO_CFG_T;
Nsent = Pktio_send( handle, TI_PKT, metadata*. &err)
Nsent = pktio_sendMulti( PKTIO_handle, TI_PKT *, metadata** , npkts , &err) [untested in release 1]
Recv Callback: recv_pkts( PKTIO handle, TI_PKT * p_recv[], metadata [], int * n_pkts, timestamp)
---internal (called by main loop/scheduler) –
pktio_poll(PKTIO handle, parmeters, &err) // poll a particular channel
pktio_pollAll(netapi_handle, parameters, &err) //poll all RX channels in this instance
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: <number>

## Slide 20: Packet i/o library (continued)
Notes:
  For packets in/out from NETCP, API implementation will create the default pktio channels. [names will be well known e.g, “NETCP_TX”, “NETCP_RX” ].
  application will call pktio_open() on these to get handles to them and to set callbacks
  Flags on open, create will say readonly, writeonly, readwrite.
    Readwrite would work for callback channels, e.g.. if application wanted to break processing path up into stages.
  Application can create additional RX channels for NETCP packets. These will need to be configured into NETCP lookups via the netcp cfg api
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: <number>

## Slide 21: Pktio library, continued
PKTIO Metadata
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
typedef struct PKTIO_METADATA_Tag { int flags1; #define PKTIO_META_RX 0x01 #define PKTIO_META_TX 0x02 union { nwalRxPktInfo_t * rx_meta; nwalTxPktInfo_t * tx_meta; } u; } PKTIO_METADATA_T; nwalRxPktInfo_t, nwalTxPktInfo_t are in: ti/drv/nwal/nwal.h

## Slide 22: Pktio library, metadata continued
RX Metadata
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
nwal_AppId | appId => LSB gives logical MAC interface packet arrived on. High order bits FUTURE
Ti_Pkt * | pPkt => pointer to packet
nwal_rxFlag1_t | rxFlag1 => gives checksum results
nwal_macPktType_t | pktType=> future (broadcast, multicast, etc)
uint32_t | startOffset
uint32_t | pktLen
uint16_t | l3OffBytes => where L3 header starts
uint16_t | l4ProtoType =>L4 protocol
uint16_t | l4OffBytes => where L4 header starts
uint16_t | ploadOffBytes => offset to L4 payload
uint16_t | ploadLen => length of payload
nwal_enetPort_t | enetPort =>physical port pkt arrived from (FUTURE)

## Slide 23: Pktio library, metadata continued
TX Metadata
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Ti_Pkt * | pPkt
nwal_txFlag1_t | txFlag1 //set bits to offload TX checksums
nwal_enetPort_t | enetPort //physical port to send to (future)
uint32_t | startOffset
uint32_t | pktLen
uint16_t | outerIpOffBytes
uint16_t | espOffBytes
uint16_t | ipOffBytes
uint16_t | l4OffBytes for L4 checksum
uint16_t | l4HdrLen for L4 checksum
uint16_t | pseudoHdrChecksum for L4 checksum
uint16_t | ploadOffBytes for L4 checksum
uint16_t | PayloadLen for L4 checksum

## Slide 24: Pktio Example
//Open a pktio channels
  /* open netcp default tx, rx queues */
  netcp_tx_chan= pktio_open(netapi_handle, NETCP_TX, NULL, &netcp_tx_cfg, &err);
  netcp_rx_chan= pktio_open(netapi_handle, NETCP_RX, (PKTIO_CB) recv_cb, &netcp_rx_cfg, &err);
//send a packet
  /* set up meta data */
  meta_tx.txFlag1 = (NWAL_TX_FLAG1_DO_IPV4_CHKSUM | NWAL_TX_FLAG1_DO_UDP_CHKSUM);
  meta_tx.startOffset = 0;
  meta_tx.pktLen = len;
  meta_tx.ipOffBytes = TEST_PKT_IP_OFFSET_BYTES;
  meta_tx.l4OffBytes = TEST_PKT_UDP_OFFSET_BYTES;
  meta_tx.l4HdrLen = TEST_PKT_UDP_HDR_LEN;
  meta_tx.ploadOffBytes = TEST_PKT_PLOAD_OFFSET_BYTES;
  meta_tx.ploadLen = TEST_PAYLOAD_LEN;
  meta_tx.pseudoHdrChecksum =
  test_utilGetIpv4PsudoChkSum(pIpHdr,(TEST_PAYLOAD_LEN+TEST_PKT_UDP_HDR_LEN));
  meta.u.tx_meta=&meta_tx;
  pktio_send(netcp_tx_chan,tip,&meta,&err);
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 25: Pktio Example (continued)
//process a received packet metadata
Received_ iface = ((unsigned int)p_meta->u.rx_meta->appId) &0xff; //last byte is interface num
Received_ipcsum =(p_meta->u.rx_meta->rxFlag1 & NWAL_RX_FLAG1_IPV4_CHKSUM_VERIFY_MASK )== NWAL_RX_FLAG1_IPV4_CHKSUM_VERIFY_ACK ? 1 : 0;
Received_l4csum = (p_meta->u.rx_meta->rxFlag1 & NWAL_RX_FLAG1_L4_CHKSUM_VERIFY_MASK )== ((NWAL_RX_FLAG1_L4_CHKSUM_VERIFY_ACK) << NWAL_RX_FLAG1_L4_CHKSUM_VERIFY_SHIFT) ? 1 : 0;
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 26: IPC Library
IPC used for:
  Packets to/from SP
  Config messages to/from SP
  Other ipc (fp core to fp core) if required
  Data to be transmitted from application to network (dsp, non-6wind fp cores)
  Internal to netapi
Same api as pktio.
  Data being send doesn’t need to be a packet..
  Meta data not used
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 27: NETCP Security Library
MARCH RELEASE
Handle= Sec_Open(netcp_handle, & err) //at startup..(creates, pktio channel internally)
Sec_Configure ( handle, .. , pointer to callback function for sideband mode)
  Callback: acc_done( TI_PKT, metadata, cookie, timestamp) //results in meta data
SAHandle= Sec_Create_SA(handle, .. ) // create a security association
Sec_Delete_SA(SAHandle) //delete a security association
Policy_handle= Sec_Create_RX_Policy(handle, ..)
Sec_Delete_RX_Policy( policy_handle)
Sec_Apply_Sideband_Crypto(TI_PKT, SAHandle , cookie)
Sec_Close(handle) //clean up at shutdown
Sec_poll (handle, parameters) // low level poll for security events
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: Align on SA, policy structures to avoid too many conversions [see at least one -> 6wind format to h/w format]
No synchronous crypto -> OK ? YES
Think about generating sequence # at same time as doing sideband encrypt. Also do the rx window check in side band mode.
<number>

## Slide 28: Security Library Examples
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: <number>

## Slide 29: Netcp Configuration
Used to create MAC interfaces and attach IP addresses
Can also be used to set up multiple RX queues from NETCP.
  Packets directed to queues based on lookup table entries
Basic Concepts:
  FLOW:
    list of pktlib heaps (of different sizes)
    Default flow setup in netapi_init
  ROUTE:
    Pktio channel (open for reading) to use as destination AND FLOW
    Default route created by netapi_init
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: DAL> add statistics stuff. ->
Idea: for tx set meta data to tell us to what fields to update. Eg index plus action
<number>

## Slide 30: Netcp configuration (continued) API
To create a logical mac interface:
NETCP_CFG_MACIF_T netcp_cfgCreateMacInterface(
  NETAPI_T h, //netapi instance
  uint8_t *p_mac, // mac address
  int iface_no, //0, 1, ,2 … (managed by application)
  int switch_port, // (physical switch port associated with this logical interface, or 0 for don’t care)
  NETCP_CFG_ROUTE_HANDLE_T route, //use NULL for default route
  NETCP_CFG_VLAN_T vlan, //FUTURE
  int state, //FUTURE
  int *err)
To attach an IP address to the interface. IP address can be qualified by TOS byte, L4 protocol, or V6 flow id (e.g., to give QOS levels their own destination pktio channel )
NETCP_CFG_IP_T netcp_AddIp(
  NETAPI_T h, //netapi instance
  int iface_no, //interface number for associated MAC address
  nwal_IpType ipType, //V4or V6
  nwalIpAddr_t *ip_addr, // the ip address
  nwalIpOpt_t *ip_qualifiers, //ip qualifiers: 0 or TOS/L4 Proto/ V6 flow id
  NETCP_CFG_ROUTE_HANDLE_T route, //use NULL for default route
  int *err)
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 31: NETCP Configuration (continued): APIs
Poll for NETCP Configuration Responses (needs to be in event loop)
  void netapi_netcpPoll (NETAPI_T p)
Request Stats
  void netcp_cfgReqStats (
    NETAPI_T h,
    NETCP_CFG_STATS_CB c,
    int doClear,
    int *err)
NETCP_CFG_STATS_CB:
  typedef void(*) NETCP_CFG_STATS_CB (
    NETAPI_T h,
    paSysStats_t *pPaStats)
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 32: NETCP CFG (continued): Advanced Configuration APIs [Available in March]
  Netcp_cfg_add_flow, del_flow:
    Flow is a list of heaps where h/w should look for free buffers.
    Default flow is created already
  Netcp_cfg_add_route,del_route
    Route = flow + destination pktio channel.
    Default created already ( pktio channel = NETCP_RX)
  Netcp_cfg_delMacInterface() //close a mac interface
  Netcp_cfgDelIp() // detach IP address
  Netcp_cfgClose() //brute force cleanup
  Netcp_cfg_addClassifier() //add a classifier. This can be used to route a packet flow to a particular pktio channel, use a specific pktlib heap, and/or have NETCP attach a tag (classifier id) to the packet. Tag will be 0 .. 2^16
    Tag will show up in the RX meta data (AppId field).
  Netcp_cfg_delClassifier() //remove the classifier
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 33: NETCP Configuration Examples
/* add mac intefaces */
netcp_cfgCreateMacInterface(
netapi_handle, //our netapi instance
&mac0[0], //mac address
0,0, //interface 0, don’t care which physical interface
(NETCP_CFG_ROUTE_HANDLE_T) NULL, //use default route
(NETCP_CFG_VLAN_T ) NULL , //future
1, //state=1 (operational)
&err);
//attach an IP to this interface
netcp_addIp(
netapi_handle, //our netapi instance
0, //mac interface index
nwal_IPV4, //IPV4
&OurIp0, //ip address
NULL, //no qualifier: all IP
(NETCP_CFG_ROUTE_HANDLE_T) NULL, //use default route
&err
);
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 34: Utilities
Cache Management: March
Get cpu frequency: available from netapimod, /debug/davinci-clocks
Pmu ccnt read
Get core id: March
Synchronization API
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Notes: <number>

## Slide 35: Synchronization Primitives
Spinlocks: map to ldrex, strex underneath
spinlock_init(x)
spinlock_lock(x) // waits until unlocked and then locks
spinlock_trylock(x) // try an get lock one time
spinlock_unlock(x) // unlocks
spinlock_is_locked(x) // is it locked ?
#
Rwlocks: map to ldrex, strex underneath
rwlock_init(x)
rwlock_read_lock(x)
rwlock_read_unlock(x)
rwlock_write_lock(x)
rwlock_write_unlock(x)
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Build around __sync_lock_test_and_set(),
__synch_lock_release()
Build around __sync_lock_test_and_set(),
__synch_lock_release()

## Slide 36: Synchronization, continued
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>
Atomic ops 32/64
atomic_read(v)
atomic_set(v, i)
atomic_add(v, i)
atomic_sub(v, i)
atomic_inc(v)
atomic_dec(v)
atomic_add_return
atomic_sub_return(v, i)
  Use GNU functions: __sync_xxx_and_fetch. ()
atomic_inc_and_test(v)
atomic_dec_and_test(v)
atomic_test_and_set(v)
  Use GNU function: __sync_vl_compare_and_swap ?
atomic_clear(v)
cmpset32(v, old, new)
  Use GNU function: __sync_vl_compare_and_swap ?
Notes: <number>

## Slide 37: Synchronization, continued
Memory barrier
mb()
rmb()
wmb()
  Map full barrier (mb) to GNU __sync_synchronize()
  For now wmb,rmb also map to this.
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 38: NETAPI Feature by Release
Feb 1 (Release 1) | Feb 21st (TBD) | March 15
One thread only |  | Multi thread (one process)
pktlib |  | Pktlib
Pktio |  | Pktio optimized
Rx/Tx checksum offload |  | 
Synchlib (basic test) |  | Synchlib optimized
Timerlib (basic) |  | Timerlib optimized
Scheduler (basic/sample) |  | 
Uncached |  | Cached memory (code/data)
Mess on exit |  | Clean shutdown, del_xxx
No security | Ipsec/policy offload | Ipsec/policy offload, crypto sideband
Add interface (mac) |  | Remove interface
Attach IP to interfaced |  | Remove IP
 |  | Add Classifier, Remove Classifier
Stats (netcp) |  | 
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>

## Slide 39: Release 1 Limitations
Limited re-execution of user space application/netapi library before reboot due to lack of graceful shutdown/cleanup of h/w.
  At most 30 re-executions of application before reboot required.
  Reboot may be required sooner if:
    Memory map of buffers/descriptors changed (e.g. netapi_tune.h parameters changed)
    Different mac, ip addresses are configured (old ones are still in h/w lookups)
    Mixing applications (e.g. running main application and then running supplied test application).
    “weird” behavior
07/29/26
“TI Proprietary Information - Strictly Private” or similar placed here if applicable
<number>